## Slide 1
Spectral Imaging
Applications & Future Trends
Remote Sensing • Environmental Monitoring • Precision Agriculture Biomedical Imaging • Industrial Sorting • Miniaturization • Real-time AI
Technical English Presentation
Based on 6 research papers (2003–2025)

## Slide 2
Outline
Presentation Structure
1
Introduction to Spectral Imaging
2
Application: Remote Sensing
3
Application: Environmental Monitoring
4
Application: Precision Agriculture
5
Application: Biomedical Imaging
6
Application: Industrial Sorting
7
Future Trend: Miniaturization
8
Future Trend: Real-time Processing & AI
9
Future Trends & Summary
2 / 16

## Slide 3
What is Spectral Imaging?
Fundamentals
Definition
Spectral imaging integrates imaging with spectroscopy, acquiring a spectral curve for each pixel to form a 3-D "spectral data cube" (2 spatial + 1 spectral dimension), enabling identification of material composition and spatial distribution.
Source: Mukhtar et al., 2025, p.1
Three Types by Number of Bands
Panchromatic
Single band High spatial resolution Limited spectral info
Multispectral (MSI)
3–25 discrete bands Medium spectral resolution
Hyperspectral (HSI)
Hundreds of contiguous narrow bands Fine spectral discrimination
Key Evolution: Multispectral → Hyperspectral
Hyperspectral imagers employ hundreds of contiguous bands to detect and identify a variety of natural and man-made materials (Shaw & Burke, 2003, p.1).
Shaw & Burke, 2003; Mukhtar et al., 2025
3 / 16

## Slide 4
Application 1: Remote Sensing
Shaw & Burke, 2003
Background & Motivation
Spectral imaging arose as an alternative to high-spatial-resolution, large-aperture satellite imaging systems, using spectral signatures rather than spatial shapes to classify ground cover.
Sensor Evolution Timeline
1972 — Landsat-1
First spaceborne multispectral imager
1987 — AVIRIS
First airborne hyperspectral imager (full solar-reflective)
2000 — Hyperion
First spaceborne HSI, 220 bands, 30 m GSD
Three Major Application Categories
• Anomaly Detection — isolate uncommon features (e.g., man-made materials in natural backgrounds)
• Target Recognition — identify specific materials using a priori spectral libraries
• Background Characterization — holistic scene analysis: land, ocean, and atmosphere
Shaw & Burke, 2003, pp.1, 9, 13-14, 19-20
4 / 16

## Slide 5
Application 2: Environmental Monitoring
Tolentino et al., 2025 — Uranium Mine Site
Case: Mary Kathleen Uranium Legacy Mine, Australia
Tailings storage facility (~1.3 km², 5.5–7.5 Mt tailings) with acid mine drainage and heavy metal / radionuclide migration risks.
Drone-Based HSI System
• Sensor: HySpex Mjolnir VS-620
• Range: VNIR–SWIR, 400–2500 nm, 410 bands
• Spatial resolution: 6–10 cm/pixel (120 m altitude)
• Centimetre GSD reduces mixed-pixel effects
Processing Methods
• SAM (Spectral Angle Mapper)
• Data-driven; classifies by spectral angle to endmembers
• BR (Band Ratios)
• Knowledge-driven; reactivity & clay-mixture indices
Key Results
• SAM differentiated mineral endmembers (gypsum, chlorite, clay) in visually uniform areas
• Mapped evaporite salt deposition pathways along surface water flow
• Identified degradation points of evaporation pond (EP) and tailings barriers — guides remediation
Tolentino et al., 2025, pp.1, 5-6, 9-16
5 / 16

## Slide 6
Application 3: Precision Agriculture
Raja et al., 2025 — Robotic Weed Control
Challenge: Crop–Weed Differentiation in High-Density Fields
In organic farming, crop and weed foliage intertwine, defeating conventional classifiers — especially in celery.
Innovation: Crop Signaling with Rhodamine B (Rh-B)
Pre-transplantation treatment of celery seedlings with Rh-B, a fluorescent compound producing machine-readable signals. Imaging uses a photometric monochrome camera + green LEDs (523 nm) + bandpass filter (575/25 nm). Conveyor speed 2.4 km/h mimics tractor field speed.
Outstanding Results
100%
Crop–Weed Accuracy
No false positives across 313 images
99.66%
Stem Location Precision
Avg. error 3.58 mm
30 ms
Processing Time / Frame
Enables real-time robotic weeding
Raja et al., 2025, pp.1, 3-4, 8-9
6 / 16

## Slide 7
Application 4: Biomedical Imaging
Tran & Fei, 2023
Why Spectral Imaging in Biomedicine?
Reveals physiological processes beyond RGB: metabolic processes, retinal oxygen saturation, tumors (skin/tongue/mucosa), and ischemia (intestine & brain). Non-ionizing, minimally invasive (VIS-NIR).
Compact / Ultracompact Definition
Compact: ≤ 5 kg (no external lens/cables) Ultracompact: < 500 g
Key Application Areas
• Skin Cancer Diagnosis
• 100% sensitivity, 85% specificity (10 bands, 63+183 images)
• Wound & Burn Healing
• Hemoglobin concentration & oxygenation over 2 weeks
• Retinal Diseases
• Oxygen saturation repeatability SD = 1.4%
• Surgical Guidance
• Laparoscopic HSI: SNR 30–43 dB, 4.6 s acquisition
• Tumor Diagnosis
• NIR-II (1000–1700 nm) enhances tumor-to-background ratio
Tran & Fei, 2023, pp.2, 28-34; Mukhtar et al., 2025, pp.5-6
7 / 16

## Slide 8
Application 5: Industrial Sorting
Romaniello et al., 2024 — Gluten-Free Legumes
Problem: Separating Gluten Contaminants from Legumes
Celiac disease drives demand for gluten-free food. Must fully remove wheat/barley/oat from faba beans, chickpeas, and lentils — mechanical separation fails due to uneven shape/color.
Why HSI in Food Industry?
Speed, objectivity, low cost, and non-destructive — enables analysis of the entire production batch.
Lab HSI System & Classifier
• VIS/NIR: 400–1000 nm; SWIR: 1000–1700 nm (InGaAs)
• FS-MRMR feature selection + SVM-linear classifier
• 100% Correct Classification Rate (CCR) across all 6 datasets
Industrial Sorter Validation
• 2× NIR cameras (15,000 Hz, 0.06 mm) + 2× RGB cameras (16M colors)
• Free-fall detection + compressed-air ejection of contaminants
Industrial Test Results
FPR = 0%
False Positive Rate — no contaminants pass
TPR > 99% | FNR 0.33–0.64%
(minimal product waste)
Romaniello et al., 2024, pp.1-3, 5, 7-10
8 / 16

## Slide 9
Future Trend 1: Miniaturization
Mukhtar et al., 2025
Four Major Hardware Design Trends
DIY
COTS camera + off-the-shelf optics + 3D printing
✓ Advantage
Low-cost, customizable
✗ Limitation
Large mechanical tolerance, tedious calibration
Freeform Optics
Dispersion + aberration + focusing in one non-axisymmetric surface
✓ Advantage
Wide FOV, high fidelity, meets CubeSat/UAV limits
✗ Limitation
High manufacturing cost, long lead time
Filter-on-Chip
Fabry-Pérot / photonic crystal filters monolithically on CMOS
✓ Advantage
No moving parts, true snapshot, high SWaP efficiency
✗ Limitation
Difficult large-area nanofabrication
Metasurface
Subwavelength meta-atoms for spectral/polarization/computational control
✓ Advantage
Ultrathin, multifunctional, video-rate HSI
✗ Limitation
nm-precision fabrication across cm apertures
From 48 kg (1972 MSS) to < 30 g snapshot cameras — progress driven by manufacturing maturity, not new optical architectures.
Mukhtar et al., 2025, pp.1, 51; Tran & Fei, 2023, p.7
9 / 16

## Slide 10
Future Trend 2: Real-time Processing & AI
Mukhtar et al., 2025
Demand for Real-time Spectral Analysis
Industrial Sorting
NIR cameras at 15,000 Hz Free-fall detection
Romaniello et al.
Precision Weeding
30 ms per frame Real-time robotic control
Raja et al.
Surgical Guidance
Acquisition as low as 4.6 s SNR 30–43 dB
Mukhtar et al.
AI & Computational Imaging Integration
• Computational spectral reconstruction: compressed sensing & deep learning demultiplexing reduce hardware burden without losing spectral resolution.
• Edge Intelligence: ML models embedded directly in handheld/UAV devices for on-site, real-time analysis (e.g., plant health, pollutant detection).
• Algorithm-Hardware Co-Design: physics-aware neural networks on ASICs → sub-Watt on-device spectral analytics for autonomous drones and handheld diagnostics.
Mukhtar et al., 2025, pp.2, 51-52
10 / 16

## Slide 11
Future Trends 3: Other Key Directions
Mukhtar et al., 2025; Tran & Fei, 2023
Tunable Metasurfaces
Reconfigurable spectral response in real time based on task requirements, with minimal size/power increase.
Mukhtar 2025
Expanded Spectral Coverage
Extend from VIS-NIR to ultraviolet and mid-infrared — unlocks astronomy, chemical sensing, security.
Mukhtar 2025
Low-Cost & Open-Source
COTS components, 3D printing, open hardware/software, smartphones as camera + control + IoT node.
Tran & Fei 2023
Multimodal Fusion
Combine with OCT (depth), LSCI (vasculature), Raman (chemistry), photoacoustic (up to 5 cm penetration).
Tran & Fei 2023
IoT & Edge Networks
UAV swarms / field sensors process data locally, transmit only key insights for scalable environmental monitoring.
Mukhtar 2025
Scalable Manufacturing
Roll-to-roll nanoimprint, high-throughput DUV lithography, open calibration protocols → mass-market products.
Mukhtar 2025
Mukhtar et al., 2025, pp.51-52; Tran & Fei, 2023, pp.35-38
11 / 16

## Slide 12
Summary
Key Takeaways
Spectral Imaging: From Remote Sensing to Diverse Fields
Applications & Key Results
• Remote Sensing
• Anomaly detection, target recognition, background characterization
• Environmental Monitoring
• Drone HSI maps uranium mine contamination at cm-scale
• Precision Agriculture
• 100% accuracy, 30 ms/frame with Rh-B crop signaling
• Biomedical Imaging
• 100% skin-cancer sensitivity; surgery at 4.6 s
• Industrial Sorting
• 0% FPR, >99% TPR for gluten-free legume sorting
Future Trends
• Miniaturization
• DIY / Freeform Optics / Filter-on-Chip / Metasurface
• Snapshot cameras (< 30 g) & on-chip integration
• Real-time Processing + AI
• Edge intelligence & algorithm-hardware co-design
• Sub-Watt on-device spectral analytics
• Other Directions
• Tunable metasurfaces, UV/MIR expansion, low-cost, multimodal fusion, IoT networks, scalable manufacturing
All papers: 2003–2025
12 / 16

## Slide 13
References
Source Papers
[P1] Shaw, G.A.; Burke, H.K. "Spectral Imaging for Remote Sensing." Lincoln Laboratory Journal, 14(1), 2003.
[P2] Tolentino, V.; Ortega Lucero, A.; Koerting, F.; Savinova, E.; Hildebrand, J.C.; Micklethwaite, S. "Drone-Based VNIR–SWIR Hyperspectral Imaging for Environmental Monitoring of a Uranium Legacy Mine Site." Drones, 9, 313, 2025.
[P3] Raja, R.; Su, W.-H.; Slaughter, D.C.; Fennimore, S.A. "Real-time precision crop identification in high weed-density environments for robotic weed control using spectral fluorescence imaging in celery." Computers and Electronics in Agriculture, 231, 110022, 2025.
[P4] Tran, M.H.; Fei, B. "Compact and ultracompact spectral imagers: technology and applications in biomedical imaging." Journal of Biomedical Optics, 28(4), 040901, 2023.
[P5] Romaniello, R.; Barrasso, A.E.; Perone, C.; Tamborrino, A.; Berardi, A.; Leone, A. "Optimisation of an Industrial Optical Sorter of Legumes for Gluten-Free Production Using Hyperspectral Imaging Techniques." Foods, 13, 404, 2024.
[P6] Mukhtar, S.; Arbabi, A.; Viegas, J. "Compact Spectral Imaging: A Review of Miniaturized and Integrated Systems." Laser & Photonics Reviews, 2025.
13 / 16

## Slide 14
Thank You
Questions & Discussion
Spectral Imaging: Applications & Future Trends